## Slide 1: Saving Energy in Cotton Gins
Paul A. Funk, Robert G. Hardin IV, and Albert A. Terrazas

## Slide 2: Energy
Energy costs represent 20% of the total cost of post-harvest processing.
A national industry survey indicated:
Electricity cost varied from $1.62 to $21.58
Fuel costs from $0.23 to $9.07 per bale

## Slide 3: Energy
Energy costs represent 20% of the total cost of ginning; a national industry survey indicated:
Electricity cost varied from $1.62 to $21.58
Fuel costs from $0.23 to $9.07 per bale
Huge disparities = huge opportunities!

## Slide 4
Study locations across US cotton belt

## Slide 5: Energy
Two types: electricity (2009-2011) and fuel (2016-2018)
Two tools: audits and monitoring studies

## Slide 6: Energy Audits
An audit is a snapshot – one moment in time
An audit quantifies energy consumption
Resolution depends on sample size
Typical cotton gin has ~120 motors and ~8 burners – we measured all
An audit asks, “What proportion is consumed by each subsystem?”
Differences between facilities due to infrastructure

## Slide 7: Energy Monitoring
A monitoring study is like a video
It records changes in energy consumption
Resolution depends on sampling rate
Monitoring asks, “What might be causing the change?”
Differences with time due to operating parameters

## Slide 8: Electricity: Rationale
Electricity is about 13% of the total cost of post harvest processing

## Slide 9: Electricity: Audit Methods
Open motor control boxes
Ammeters measure current
Record values
P = V*I*√3

## Slide 10: Electricity: Monitoring Methods
Ammeter transmits current signal
Logger records values

## Slide 11: Electricity: Results
Electrical Energy Consumed (kWh/b)
1962 1982 2009
Seed Cotton Cleaning 2.6 5.4 2.9
Saw Ginning 8.5 7.0 6.4
Lint Cleaning 7.7 4.6 2.4
Bale Packaging 5.8 4.0 4.7
Materials Handling 22.9 31.0 23.2
Per Bale Total 47.5 52.0 39.5
Connected Power (hp) 764 1,709 3,030 ^ 4x

## Slide 12: Electricity: Results
Electrical Energy Consumed (kWh/b)
1962 1982 2009 2009
Seed Cotton Cleaning 2.6 5.4 2.9 7%
Saw Ginning 8.5 7.0 6.4 16%
Lint Cleaning 7.7 4.6 2.4 6%
Bale Packaging 5.8 4.0 4.7 12%
Materials Handling 22.9 31.0 23.2 59%
Per Bale Total 47.5 52.0 39.5
Connected Power (hp) 764 1,709 3,030

## Slide 13: Electricity: Results
Plug leaks
Seal covers and access doors
Repair vacuum dropper flashings

## Slide 14: Results - ELECTRICITY
Upgrade fans (that handle air only)

## Slide 15: Electricity: Results
Simplify ductwork

## Slide 16: Electricity: Results …avoid chaos

## Slide 17
Flow Compliments Rotation
Flow Fights Rotation
Long Sweep Elbows
Turbulent Inlet
Laminar Flow Inlet
Long
Sweep
Elbows
Electricity: Results - Reduce Fan Turbulence in/out

## Slide 18
Rectangular evasé
Radial evasé
Spin Cap

## Slide 19: Electricity: Results
Match motor sizes to loads
Buy high efficiency motors, but only when replacement is needed

## Slide 20: Electricity: Results
Mechanical conveying wherever practical

## Slide 21: Electricity: Impacts
Industry has responded to rising costs by increasing efficiency
Electricity consumption per bale has decreased 0.6 kWh each year
Improved sustainability and environmental stewardship
National savings about $10 million each season

## Slide 23
Fuel: Rationale …big gas meter

## Slide 24
Fuel: Rationale …big propane tank

## Slide 25: Fuel: Rationale
Fuel = 6½ % to 8½ % of ginning cost
Prices volatile, propane doubled in 10 y; can’t control cost of fuel
Weather unpredictable; can’t control drying amount needed
Fuel = most variable cost = biggest threat to profitability

## Slide 26: Fuel: Rationale
Fuel = 6½ % to 8½ % of ginning cost
Prices volatile, propane doubled in 10 y; can’t control cost of fuel
Weather unpredictable; can’t control drying amount needed
Fuel = most variable cost = biggest threat to profitability
    Can we improve utilization?

## Slide 27: Fuel: Rationale
Fuel Use Audits in Commercial Gins: in-season
It would be disruptive to cut gas flow to install a meter on each burner while the gin is running
Fuel Use Audits in Commercial Gins: repair-season
It would be expensive to install meters on every burner in every cooperating commercial gin

## Slide 28: Fuel: Methods
Proxy fuel use: velocity pressure and air temperatures
  Velocity pressure & density → velocity
  Velocity & pipe diameter → volumetric flow
  Volumetric flow & density → mass flow
  Mass flow, temperature change, & burner efficiency → fuel used

## Slide 32: Fuel: Methods
Quantify fuel consumption
Quantify effective drying
  Bales per hour & turnout → seed cotton mass flow rate
  Change in moisture content of that mass flow → water evaporated
  Enthalpy of vaporization & rate of evaporation → benefit (kW)

## Slide 36: Fuel: Methods
Quantify fuel consumption
Quantify effective drying
Estimate portion of energy used for drying (fuel use efficiency)
  Drying benefit/Fuel used cost → efficiency

## Slide 37: Fuel: Methods
Quantify fuel consumption
Quantify effective drying
Estimate portion of energy used for drying (fuel use efficiency)
Find operating strategies, equipment selections, and facility designs that use fuel more efficiently

## Slide 38: Fuel: Results
Find operating strategies, equipment selections, and facility designs that use fuel more efficiently
…hasn’t been as easy as it first looked
  Weather
  Crop condition
  Unmeasured factors

## Slide 39
Chart: Two Stages, Separate Burners
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | AVG
 | 0.074612 | 0.079237 | 0.077719 | 0.078701 | 0.078842 | 0.07494 | 0.073053 | 0.07296 | 0.073647 | 0.072082 | 0.070036 | 0.068805 | 0.068963 | 0.070814 | 0.070315 | 0.071025 | 0.076392 | 0.074101 | 0.076431 | 0.074447 | 0.069862 | 0.073211 | 0.069254 | 0.069624 | 0.07162 | 0.073099 | 0.068548 | 0.066277 | 0.066199 | 0.069548 | 0.072479
 | 0.064449 | 0.070292 | 0.072628 | 0.070802 | 0.067414 | 0.068569 | 0.063311 | 0.063637 | 0.064754 | 0.065582 | 0.065264 | 0.061769 | 0.06136 | 0.062978 | 0.059263 | 0.067379 | 0.067634 | 0.066754 | 0.068916 | 0.064798 | 0.06176 | 0.060072 | 0.056867 | 0.061255 | 0.06158 | 0.062258 | 0.061989 | 0.059623 | 0.060693 | 0.054741 | 0.063946 | 0.063808 | 0.0086705
 | 0.062672 | 0.067816 | 0.070697 | 0.07458 | 0.070224 | 0.062897 | 0.06347 | 0.064076 | 0.065658 | 0.06332 | 0.060477 | 0.061557 | 0.061975 | 0.059016 | 0.058851 | 0.067153 | 0.070012 | 0.069405 | 0.065969 | 0.06676 | 0.063465 | 0.057095 | 0.058291 | 0.061533 | 0.063616 | 0.059645 | 0.057744 | 0.059712 | 0.061991 | 0.060431
 | 0.054569 | 0.057548 | 0.058784 | 0.060309 | 0.059718 | 0.055319 | 0.055218 | 0.05691 | 0.057181 | 0.053797 | 0.053032 | 0.054408 | 0.054755 | 0.053593 | 0.05198 | 0.056243 | 0.057914 | 0.056771 | 0.057892 | 0.055109 | 0.052901 | 0.054541 | 0.050756 | 0.050949 | 0.053689 | 0.053781 | 0.05045 | 0.048487 | 0.05213 | 0.05062
Notes: Two stages of drying each with their own burners were nearly equal in effectiveness. Each stage used about the same amount of fuel. This provides the gin with more drying capacity if conditions require it. Both of these examples ginned at 5.5% moisture content, wet mass basis.

## Slide 40
Chart: One Burner: Skimmed Air from 1st Stage used in 2nd Stage
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
 | 0.069185 | 0.060682 | 0.062904 | 0.064391 | 0.064115 | 0.070376 | 0.066806 | 0.068804 | 0.067243 | 0.060447 | 0.065861 | 0.064196 | 0.067119 | 0.067997 | 0.064526 | 0.06972 | 0.074168 | 0.066314 | 0.060786 | 0.067199 | 0.0697 | 0.075213 | 0.077642 | 0.078128 | 0.08131 | 0.078128 | 0.075491 | 0.073489 | 0.068496 | 0.069345
 | 0.054325 | 0.052682 | 0.052045 | 0.056232 | 0.057232 | 0.057724 | 0.057553 | 0.061652 | 0.058965 | 0.052786 | 0.057935 | 0.055773 | 0.057382 | 0.063125 | 0.05472 | 0.059815 | 0.063509 | 0.055367 | 0.055409 | 0.055328 | 0.062667 | 0.06159 | 0.064956 | 0.072745 | 0.067053 | 0.06486 | 0.064223 | 0.058213 | 0.060019
 | 0.052947 | 0.053786 | 0.051923 | 0.050263 | 0.053507 | 0.055497 | 0.053353 | 0.055795 | 0.054194 | 0.05318 | 0.051521 | 0.050603 | 0.053984 | 0.054467 | 0.05188 | 0.056028 | 0.056844 | 0.052116 | 0.054355 | 0.051103 | 0.053097 | 0.057666 | 0.058786 | 0.060611 | 0.062309 | 0.062105 | 0.058958 | 0.055276 | 0.052678 | 0.05525
Notes: Warm moist air from first stage of drying was skimmed and used to convey seed cotton to the second stage of cleaning. The second stage is half (40%) as effective as the first stage, but it required no additional fuel. This works fine in dry climates.

## Slide 41
Chart: Three Stages, 3rd stage burners turned off
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
 | 0.073448 | 0.074172 | 0.07279 | 0.073344 | 0.076388 | 0.074162 | 0.074117 | 0.073818 | 0.07704 | 0.077864 | 0.077618 | 0.077738 | 0.080819 | 0.074755 | 0.076589 | 0.07102 | 0.079699 | 0.071077 | 0.075337 | 0.070083 | 0.071432 | 0.069681 | 0.070299 | 0.073072 | 0.068425 | 0.073044 | 0.070088 | 0.065671
 | 0.06658 | 0.062098 | 0.064381 | 0.060813 | 0.070717 | 0.071894 | 0.065624 | 0.073202 | 0.06677 | 0.067455 | 0.065375 | 0.066651 | 0.067511 | 0.07496 | 0.065536 | 0.066342 | 0.063197 | 0.062384 | 0.071454 | 0.063644 | 0.065361 | 0.062585 | 0.062755 | 0.062391 | 0.066556 | 0.066198 | 0.060099 | 0.060821
 | 0.063147 | 0.059219 | 0.057821 | 0.058298 | 0.06216 | 0.064164 | 0.062382 | 0.059686 | 0.062776 | 0.064926 | 0.062577 | 0.060484 | 0.062226 | 0.064867 | 0.06137 | 0.06041 | 0.062587 | 0.059233 | 0.067244 | 0.063457 | 0.06313 | 0.058333 | 0.056895 | 0.059348 | 0.059584 | 0.063778 | 0.058688 | 0.056477
 | 0.058399 | 0.058163 | 0.059812 | 0.057691 | 0.059779 | 0.062215 | 0.062223 | 0.061015 | 0.059851 | 0.06095 | 0.06139 | 0.061056 | 0.060137 | 0.061399 | 0.059925 | 0.059413 | 0.059081 | 0.05854 | 0.057886 | 0.061134 | 0.061976 | 0.058368 | 0.057352 | 0.056793 | 0.057558 | 0.06255 | 0.059263 | 0.054898
Notes: This gin had the capacity to do more drying than it needed to at the time of our sampling, so they had turned down the second stage and turned off the third stage burners. Even without any heat, a little bit of drying took place in the third stage from ambient air conveying the seed cotton.

## Slide 42
Chart: First Stage more Efficient
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Module Feeder | 0.074 | 0.0696 | 0.0706 | 0.0756 | 0.0714 | 0.0728 | 0.0668 | 0.0682 | 0.0732 | 0.0756 | 0.0786 | 0.0874 | 0.0848 | 0.0818 | 0.0794 | 0.0784 | 0.0752 | 0.0806 | 0.0848 | 0.0762 | 0.0738 | 0.0694 | 0.072 | 0.0708 | 0.0712 | 0.0748 | 0.0768 | 0.0722 | 0.0738 | 0.0724
Intermediate | 0.0558 | 0.0548 | 0.0519 | 0.0511 | 0.0502 | 0.0572 | 0.0734 | 0.05945 | 0.0657 | 0.0644 | 0.0635 | 0.0635 | 0.0633 | 0.0595 | 0.05625 | 0.0562 | 0.0572 | 0.06 | 0.05445 | 0.06 | 0.05905 | 0.0594 | 0.0578 | 0.0567 | 0.0541 | 0.0525 | 0.0549 | 0.0502 | 0.0528 | 0.05
Overflow A | 0.0598 | 0.0569 | 0.0544 | 0.055 | 0.0542 | 0.053 | 0.0594 | 0.0536 | 0.0516 | 0.0514 | 0.0562 | 0.0564 | 0.0574 | 0.0418 | 0.042 | 0.0554 | 0.0588 | 0.0544 | 0.053 | 0.054 | 0.0508 | 0.0504 | 0.0524 | 0.0568 | 0.0436 | 0.0456 | 0.0448 | 0.0592 | 0.057 | 0.058
2017, 1st Stage: 26%
2017, 2nd Stage: 15%

## Slide 43
Chart: Same Gin, 2 Stages, 2 Years
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 24 | 25 | 26 | 27 | 28 | 29 | 30
 | 0.0868 | 0.0956 | 0.0968 | 0.0946 | 0.0894 | 0.0718 | 0.0762 | 0.0878 | 0.0826 | 0.089 | 0.0762 | 0.0752 | 0.072 | 0.0822 | 0.0846 | 0.0888 | 0.0774 | 0.0802 | 0.0696 | 0.0818 | 0.0848 | 0.0816 | 0.08 | 0.0894 | 0.074 | 0.0864 | 0.075 | 0.076 | 0.0878 | 0.087
 | 0.072 | 0.0792 | 0.066 | 0.0832 | 0.0734 | 0.074 | 0.0848 | 0.078 | 0.074 | 0.069 | 0.0732 | 0.0808 | 0.0674 | 0.0754 | 0.07 | 0.0694 | 0.0688 | 0.0726 | 0.083 | 0.0796 | 0.069 | 0.071 | 0.0818 | 0.0698 | 0.077 | 0.067 | 0.0704 | 0.0684 | 0.0668 | 0.0724
 | 0.071708 | 0.068273 | 0.066638 | 0.069832 | 0.069544 | 0.0692 | 0.066292 | 0.065605 | 0.069521 | 0.059555 | 0.064437 | 0.065871 | 0.060848 | 0.062917 | 0.065328 | 0.064881 | 0.067267 | 0.065187 | 0.061953 | 0.056549 | 0.057441 | 0.056175 | 0.057055 | 0.054886 | 0.05602 | 0.057414 | 0.056765 | 0.058549 | 0.061099 | 0.056429
 | 0.055085 | 0.05389 | 0.053989 | 0.055196 | 0.054458 | 0.058383 | 0.054517 | 0.05422 | 0.054358 | 0.053071 | 0.055812 | 0.055025 | 0.052418 | 0.051977 | 0.05464 | 0.056443 | 0.05478 | 0.057942 | 0.053852 | 0.05054 | 0.051761 | 0.050452 | 0.050121 | 0.047262 | 0.049719 | 0.050647 | 0.053458 | 0.054135 | 0.05386 | 0.050561
Low efficiency ascribed to long, uninsulated pipe from burner to seed cotton pickup

## Slide 44
Chart: Round Modules
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
 | 0.072535 | 0.06838 | 0.069828 | 0.072084 | 0.074622 | 0.072209 | 0.061705 | 0.074824 | 0.068567 | 0.075244 | 0.068043 | 0.078026 | 0.06965 | 0.081407 | 0.079061 | 0.087723 | 0.089255 | 0.090851 | 0.091786 | 0.081021 | 0.070401 | 0.073366 | 0.073403 | 0.072497 | 0.080289 | 0.076511 | 0.079908 | 0.077656 | 0.074525 | 0.076583
 | 0.070473 | 0.068801 | 0.066989 | 0.070836 | 0.06805 | 0.059472 | 0.062175 | 0.058332 | 0.058373 | 0.061081 | 0.058741 | 0.068843 | 0.061329 | 0.066034 | 0.069908 | 0.067939 | 0.067765 | 0.067577 | 0.068316 | 0.071965 | 0.071437 | 0.070434 | 0.07774 | 0.07964 | 0.063894 | 0.062871 | 0.06344 | 0.064422 | 0.063165 | 0.066075
 | 0.066364 | 0.065571 | 0.063997 | 0.064137 | 0.062844 | 0.057577 | 0.05682 | 0.057171 | 0.05658 | 0.058018 | 0.058131 | 0.06297 | 0.06262 | 0.063345 | 0.067342 | 0.070455 | 0.070428 | 0.066955 | 0.068905 | 0.071403 | 0.06999 | 0.07394 | 0.075512 | 0.075122 | 0.064025 | 0.063486 | 0.063842 | 0.062665 | 0.061748 | 0.062206
 | 0.067831 | 0.062079 | 0.063122 | 0.06362 | 0.060897 | 0.056924 | 0.056342 | 0.054654 | 0.056323 | 0.056056 | 0.056235 | 0.061892 | 0.060639 | 0.060799 | 0.063534 | 0.064773 | 0.066569 | 0.066791 | 0.065665 | 0.065666 | 0.06744 | 0.064868 | 0.067179 | 0.07165 | 0.066581 | 0.060265 | 0.059238 | 0.05886 | 0.059941 | 0.059131
High efficiency ascribed to burners being close to dryers,
with insulated pipe from burner to pickup point
2016, 1st Stage: 43%
2017, 1st Stage: 55%

## Slide 45: Fuel: Results
Easy fruit to pick: Operation
  Ambient temperature dry air can make cotton drier, so
  Turn off the second stage when drying is not needed

## Slide 46: Fuel: Results
Easy fruit to pick: Operation
  Ambient temperature dry air can make cotton drier, so
  Turn off the second stage when drying is not needed
Easy fruit to pick: Infrastructure
  Install a burner control to save fuel when cotton is dry
  Follow ASABE Standard 530.1 for sensor locations
  Insulate the hottest pipe – from burner to mix point
  Place the burner close to the mix point

## Slide 47: Fuel: Results
Complications: Operation
  Can’t skip first stage because pre-cleaning efficiency depends on moisture content being low
Complications: Infrastructure
  Modification of major components may be cost prohibitive

## Slide 48: Fuel: Results
Persuade growers to harvest when cotton is dry

## Slide 49: Fuel: Results
Protect covers/wraps from damage
Store cotton in dry conditions

## Slide 50: USDA-Agricultural Research Service: Southwestern Cotton Ginning Research Lab (NM) US Cotton Ginning Research Unit (MS)